## Slide 1
MACHINE LEARNING COURSE PROJECT
Multi-Objective PPO-Based Receiver Energy- and SIC-Complexity-Aware NOMA Scheduling
Learning to schedule NOMA users with an RL agent that balances speed, battery life, and receiver complexity
Ranga Charvik Battagiri | Student ID: 2520040108 | Batch 2025-2029
A. Dhanush | Student ID: 2520040109 | Batch 2025-2029
R. Gnaneshwar | Student ID: 2520040076 | Batch 2025-2029
Department of Electronics and Communication Engineering • KL Deemed to be University (KLH), Hyderabad

## Slide 2
Why This Project Matters
Networks are getting crowded — and existing solutions ignore device battery limits
5G/6G Density
Massive numbers of connected IoT devices, wearables, and sensors now share the same limited spectrum.
NOMA's Trade-off
NOMA packs more users per channel using power-domain sharing — but receivers must "unmix" combined signals via SIC.
The Missing Piece
More users per cluster means more SIC decoding stages — draining battery on devices that existing schedulers ignore.

## Slide 3
How NOMA Works
Multiple users share the same time-frequency slot, separated by power level instead
Base Station
Superimposed
signal (power-multiplexed)
User A — weak channel
High power share
User B — medium channel
Medium power share
User C — strong channel
Low power share
Key idea: weak-channel users get more transmit power so their signal survives the interference; strong-channel users get less, since they can still be decoded through it.

## Slide 4
SIC: The Hidden Cost of NOMA
Every receiver must peel apart the combined signal — and that costs time, compute, and battery
1
Decode strongest
signal
2
Subtract it from
the mix
3
Decode next
strongest
4
Repeat until your
signal is isolated
More users in a cluster → more SIC stages → more decoding delay + energy drain
The Core Tension This Project Addresses
Bigger NOMA clusters improve spectral efficiency, but increase SIC stages — draining battery on devices that can least afford it (IoT sensors, wearables). Most existing schedulers optimize only throughput and ignore this cost entirely.

## Slide 5
The Research Gap
What existing NOMA scheduling literature focuses on — and what it leaves out
What's Been Studied
• Q-learning for power allocation after channel-gain clustering
• Object Migration Automata for the user-grouping sub-problem
• Joint RL-based user pairing + power allocation in MIMO-NOMA
• Power-consumption models that account for SIC energy overhead
What's Missing
• Almost all approaches optimize a single objective — usually just throughput
• SIC energy cost is treated as a fixed system parameter, not something to optimize against
• No scheduler adapts clustering decisions based on individual users' remaining battery level
→ This project's contribution: a scheduler that is explicitly rewarded for battery- and SIC-aware decisions.

## Slide 6
Project Objectives
1
Model a simplified NOMA downlink system in Python — throughput, SIC stages, and receiver energy cost
2
Formulate scheduling as a Markov Decision Process (state, action, reward)
3
Train a PPO agent with a multi-objective reward balancing throughput, energy, and SIC complexity
4
Implement random, fixed, and greedy baseline schedulers for comparison
5
Evaluate PPO vs. baselines across throughput, energy, SIC stages, and fairness

## Slide 7
Formulating It as an RL Problem
Scheduling is a repeated decision problem — a natural fit for reinforcement learning
State
Channel gain + remaining battery level of every user
Action
Which NOMA cluster each user is assigned to
Reward
Weighted combination of throughput, energy cost, and SIC stages
Policy
The PPO agent's learned scheduling strategy
Multi-Objective Reward Function
Reward = w₁ · Throughput − w₂ · Energy Cost − w₃ · SIC Stages
Used weights: w₁ = 1.0 (throughput) w₂ = 2.5 (energy) w₃ = 1.0 (SIC complexity)

## Slide 8
System Model in Detail
The three formulas that drive every scheduling decision in the simulation
Throughput (Shannon capacity)
Rᵢ = B · log₂(1 + SINRᵢ)
Higher SINR (signal vs. interference+noise) means a higher achievable rate for user i.
SIC stages per user
SICᵢ = cluster_size − 1
Every extra user sharing a cluster adds one more decoding stage the receiver must perform.
Battery-weighted energy cost
Eᵢ = (E_base + SICᵢ·E_stage) × (1 + 3·urgencyᵢ)
urgencyᵢ = 1 − batteryᵢ — a near-empty battery multiplies the penalty up to 4×.

## Slide 9
Project Workflow
From simulation to a validated, comparable result
1
Build Environment
Custom Gymnasium NOMA simulation: throughput, SIC, battery-weighted energy
2
Multi-Seed Training
Train 3 independent PPO agents; keep the best by evaluation score
3
Baseline Comparison
Run Random, Fixed, and Greedy schedulers on the same environment
4
Evaluate & Compare
30-episode averages across throughput, energy, SIC stages, fairness
Why multi-seed training? PPO can land in different quality outcomes depending on random initialization. Training several seeds and keeping only the best is standard practice for a trustworthy result, not a lucky one-off run.

## Slide 10
Implementation
Built entirely in Python, using standard, well-tested RL tooling
Gymnasium
Custom NOMA environment: reset(), step(), reward
Stable-Baselines3
PPO algorithm implementation
NumPy
SINR / throughput / energy formulas
Matplotlib
Comparison charts
Training Setup
• 6 users, 3 NOMA clusters
• 3 seeds × 200,000 timesteps, best model kept
• 128×128 policy network, decaying learning rate
Baseline Schedulers
• Random — no information used
• Fixed — equal-sized clusters, static
• Greedy — channel-gain based, still battery-blind

## Slide 11
Results: PPO vs. Baselines
Combined multi-objective score (throughput − 2.5×energy − 1.0×SIC stages), averaged over 30 episodes
Chart: 
| Random | Fixed | Greedy | PPO (ours)
Combined Score | -4.979 | -1.582 | -1.251 | -0.613
−0.613
PPO combined score
best overall trade-off
+51%
vs. Greedy baseline
improvement in combined score
0.82
Value fn. explained variance
up from ~0 before tuning

## Slide 12
Detailed Metric Comparison
Five evaluation metrics for Random, Fixed, Greedy and PPO — green bars are our PPO scheduler
Highest throughput
PPO clearly leads on average throughput, ahead of Random, Fixed and Greedy.
Best combined score
Highest multi-objective score of all four schedulers — the trade-off PPO was trained for.
Honest trade-off
Fixed and Greedy keep energy, SIC stages and fairness lower — PPO trades some for throughput.
Metrics: average throughput ↑ • energy cost ↓ • SIC stages ↓ • Jain’s fairness index ↑ • combined score ↑

## Slide 13
Why the PPO Scheduler Wins
PPO is the only scheduler that sees battery level
None of the baselines observe remaining energy at all, so they cannot protect low-battery users from being placed in large, SIC-heavy clusters — PPO can, because it's directly rewarded for it.
Honest trade-off, not a clean sweep
1
Greedy/Fixed achieve lower SIC stage counts and higher fairness — they build perfectly even clusters by construction
2
PPO achieves the highest throughput and the best combined score, but with less even cluster sizes
3
No single method should dominate every axis in a genuine multi-objective problem — what matters is the weighted trade-off PPO was trained on

## Slide 14
Conclusion & Future Work
A PPO-based scheduler that jointly optimizes throughput, receiver energy, and SIC complexity achieves a better overall trade-off than fixed heuristic rules — by being the only approach that adapts to individual users' battery levels.
Future Directions
→ Multi-cell interference and imperfect channel state information
→ Model imperfect SIC / error propagation effects
→ Add an explicit fairness term to the reward function
→ True Pareto-front multi-objective RL, beyond weighted-sum
→ Scale up to more users and clusters for realism
Ranga Charvik Battagiri • A. Dhanush • R. Gnaneshwar • Machine Learning (25SC2107E) • KLH